## Slide 1: Team 9: T9-837X Microcontroller

## Slide 2: Team 9: T9-837X Microcontroller
Charlie Van Hook
Soud Alkharji
Gidon Gautel
Yoan Zhao

## Slide 3: Goal & Motivation
Motivation: Not enough microcontrollers! (and learn system-wide skills)
Goal: Create an easily implementable microcontroller design
Use cases:
Robotics
Wearable Electronics
Control

## Slide 4: Functionality: Project Deliverables
Design Phase
  Architectural Design
    Microprocessor architecture
    Datapath components
    Control signals and timing constraints
  ISA Design
    Define supported instructions
    Map instructions to micro-operations in the datapath
  Component Design
    ALU design
    Register File design
    Control Unit design
    Memory Interface design
    Clock and Reset Circuit design
    Programmer
    Program counter
Implementation Phase
  Schematic Design
  Integration
  Timing Analysis
  Peripheral Integration
Simulation and Verification
  Testbench Development
    Write testbenches for modules
    Develop system-level testbenches
  Functional Simulation
    Verify ISA instruction execution
    Simulate edge cases and reset functionality
    Test UART-based assembly program loading
  Performance Verification
    Measure CPI and throughput
    Validate interrupt handling
FPGA Deployment
  Synthesis
  Bitstream Generation
  Programming
Physical Testing
  Test Setup
  Test Program Execution
  Debugging
Documentation
  Technical Documentation
  User Guide
  Project Report
Presentation and Deliverables
  Demonstration
  Source Code
  Simulation Results
  FPGA Configuration Files

## Slide 5: Specification: Key Design Choices
Core Functionality/Design Goals
Harvard architecture
SRAM
Instruction set: MIPS
Functionality:
  Digital I/O
  ADC
  Pulse width modulation
32-bit
Supports multiplication and division
No floats
Stretch Goals:
Multi-process functionality
Interrupt timer
Floats
Longs
Notes: Yoan

## Slide 6: Specification: Supported Assembly Instructions
R-type:
Add
Subtract
And
Or
Multiply
Divide
SLT (Set Less Than)
I-Type:
ADDI (Add Immediate)
SLTI (Set Less Than Immediate)
J-type:
JR (Jump Register)
LW (Load Word)
SW (Save Word)
BEQ (Branch if Equal-to)
BNE (Branch if Not Equal-to)
J (Jump to position)
JAL (Jump and Link)
LHI (Load High)
LLO (Load Low)
Notes: Soud

## Slide 7: System Block Diagram
Block Diagram Goes Here
Notes: Charlie

## Slide 8: Internal Block Diagram
Memory (SRAM)

## Slide 9: Code Snippets
always @(posedge clk or posedge reset) begin
if(reset)
pc_current <= 32'd0;
else
pc_current <= pc_next;
end
assign pc2 = pc_current + 31'd2;
assign im_shift_1 = {imm_ext[30:0],1'b0};
assign no_sign_ext = ~(im_shift_1) + 1'b1;
// PC beq add
assign PC_beq = (im_shift_1[31] == 1'b1) ? (pc2 - no_sign_ext): (pc2 +im_shift_1);
assign beq_control = branch & zero_flag;
assign PC_4beq = (beq_control==1'b1) ? PC_beq : pc2;
assign PC_j = {pc2[31],jump_shift_1};
assign PC_4beqj = (jump == 1'b1) ? PC_j : PC_4beq;
assign PC_jr = reg_read_data_1;
assign pc_next = (JRControl==1'b1) ? PC_jr : PC_4beqj;
How can we implement a Program Counter with jumping, branching, and waiting
Certain operations are atomic (fetching data from registers, and, or, etc) meaning they take 1 cpu cycle
Others take several(memory actions, multiplication, etc)
We need to flag the program whenever the cpu is waiting on a previous step
We also need to allow the processor to skip steps and return back for jumping operations

## Slide 10: Code Snippets (cont.)
module instruction_mem(instruction, address);
input [31:0] address;
output [31:0] instruction;
reg [31:0] instrmem[1023:0];
reg [31:0] tmp;
buf #1000 buf0(instruction[0],tmp[0]),
buf1(instruction[1],tmp[1]),
. . .
buf31(instruction[31],tmp[31]);
always @(address) begin
tmp = instrmem[address/4]
end
initial begin
$readmemb("instr.txt", instrmem);
end
endmodule
How can we use testing methodologies for a complex system in Verilog?
  I dunno but I wrote some code to help
00111000000100000000000000000011
00111000000100010000000000000100
00001000000000000000000000000101
00111000000100000000000000000001
00111000000100010000000000000001
00000010001100001001000000100010
00010110000100011111111111111100
00000010000100011001100000100000
10101110010100110000000000010000
10001110010101000000000000010000
00000010000101001010100000101010
10001110010100110000000000010000
00111010010100110000000000000001
00111010101101010000000000000001
00000010101000000000000000001000
Instr.txt, output.txt
BASH

## Slide 11: Project Successes, Improvements
Successes:
Working Processor!
  Working ALU
  ALU controller
  Jump controller
  Program counter
  Register file
  Instruction memory
  Data memory
  UART programmer
  Interrupt handler
Novel testing methods
Assembly literacy achieved
Still working on:
Peripheral bus
Testing campaign (particularly system-level & hardware testing)
Lessons learned:
Module-level testbenches do not scale well
Utilize Vivado pre-build tools to avoid unnecessary wasted time
Use Python to simplify ISA encoding
Notes: Successes: Soud, To improve on: Yoan

## Slide 12: Thank you for listening!